SECTION 02871

BICYCLE RACKS

Display hidden notes to specifier by using "Tools"/"Options"/"View"/"Hidden Text".

** NOTE TO SPECIFIER **  Saris Cycling Group; bicycle racks.

.

This section is based on the products of Saris Cycling Group, which is located at:

5253 Verona Rd.

Madison, WI 53711

Toll Free TEL: (800) 783-7257

Tel: (608) 274-6550

Fax: (608) 274-1702

Email:  prkmgr@saris.com

Web: http://www.sarisparking.com

[ Click Here ] for additional information.

Bicycle Racks:  SARIS metal racks for parking and storing bicycles: class II, and III. Formed tubing, welded and riveted grids.  Metal parking systems

GENERAL

SECTION INCLUDES

** NOTE TO SPECIFIER **  Delete items below not required for project.

Bicycle City Racks.

RELATED SECTIONS

** NOTE TO SPECIFIER **  Delete any sections below not relevant to this project; add others as required.

Section 02900 - Landscaping:  Installation location and coordination.

REFERENCES

** NOTE TO SPECIFIER **  Delete references from the list below that are not actually required by the text of the edited section.

American Society for Testing and Materials ASTM A 513 - Standard Specification for Electric-Resistance-Welded Carbon and Alloy Steel Mechanical Tubing.

American Society for Testing and Materials ASTM A 500B - Standard Specification for Cold-Formed Welded and Seamless Carbon Steel Structural Tubing in Rounds and Shapes.

SUBMITTALS

Submit under provisions of Section 01300.

[ Product Data ]:  Manufacturer's data sheets on each product to be used, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Shop Drawings:  Manufacturing details for each bicycle rack.

** NOTE TO SPECIFIER **  Delete selection samples if colors have already been selected.

Selection Samples:  For each finish product specified, two complete sets of color chips representing manufacturer's full range of available colors and patterns.

Verification Samples:  For each finish product specified, two samples, minimum size 6 inches (150 mm) square representing actual product, color, and patterns.

QUALITY ASSURANCE

Manufacturer Qualifications:

A firm experienced in manufacturing bicycle racks similar to those required for this project and with a record of successful in-service performance.

Installer Qualifications:

An experienced installer who has completed installation of bicycle racks similar in material, design, and extent to that indicated for this project and whose work has resulted in construction with a record of successful in-service performance.

Source Limitations: Obtain each color, finish, shape and type of bicycle rack from a single source with resources to provide components of consistent quality in appearance and physical properties.

** NOTE TO SPECIFIER **  Include a mock-up if the project size and/or quality warrant taking such a precaution.  The following is one example of how a mock-up on a large project might be specified.  When deciding on the extent of the mock-up, consider all the major different types of work on the project.

Mock-Up:  Provide a mock-up for evaluation of surface preparation techniques and application workmanship.

Install in areas designated by Architect.

Do not proceed with remaining work until workmanship and installation are approved by Architect.

Refinish mock-up area as required to produce acceptable work.

DELIVERY, STORAGE, AND HANDLING

Store products in manufacturer's unopened packaging until ready for installation.

Store and dispose of solvent-based materials, and materials used with solvent-based materials, in accordance with requirements of local authorities having jurisdiction.

PROJECT CONDITIONS

Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results.  Do not install products under environmental conditions outside manufacturer's absolute limits.

PRODUCTS

MANUFACTURERS

Acceptable Manufacturer:  Saris Cycling Group; 5253 Verona Rd., Madison, WI 53711.  ASD. Toll Free TEL: (800) 783-7257. Te1: (608) 274-6550.  
Fax: (608) 274-1702.  Email:  info@sarisinfrastructure.com  
Web: http://www.sarisinfrastructure.com

** NOTE TO SPECIFIER **  Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

Substitutions:  Not permitted.

Requests for substitutions will be considered in accordance with provisions of Section 01600.

BICYCLE HIGH SECURITY RACKS

** NOTE TO SPECIFIER **  Delete if not required.

Bicycle High Security Racks, City Rack 2400 Series:

Construction:  7 gauge, 2.5 inches (63 mm) square steel tube frame; 11 gauge, 1-1/2 inches by 1 inches (38 mm by  25 mm) square tube hangers.

** NOTE TO SPECIFIER **  Delete capacities not required.

Capacity:  3 bike, single side, 84 inch by 83 inch (2134 by 2108 mm) space requirement, below-grade mount.

Capacity:  3 bike, single side, 86 inch by 83 inch (2184 by 2108 mm) space requirement, free-standing/flange mount.

Capacity:  4 bike, single side, 84 inch by 108 inch (2134 by 2743 mm) space requirement, below-grade mount.

Capacity 4 bike, single side, 86 inch by 108 inch (2184 by 2743 mm) space requirement, free-standing/flange mount.

Capacity:  5 bike, single side, 84 inch by 133 inch (2134 by 3378 mm) space requirement, below-grade mount.

Capacity:  5 bike, single side, 86 inch by 133 inch (2184 by 3378 mm) space requirement, free-standing/flange mount.

Capacity:  6 bike, single side, 84 inch by 158 inch (2134 by 4013 mm) space requirement, below-grade mount.

Capacity: 6 bike, single side, 84 inch by 158 inch (2134 by 4013 mm) space requirement, free-standing/flange mount.

Capacity: 5 bike, double side, 120 inch by 83 inch (3048 by 2108 mm) space requirement, below-grade mount.

Capacity:  5 bike, double side 120 inch by 83 inch (3048 by 2108 mm) space requirement, free-standing/flange mount.

Capacity:  7 bike, double side, 120 inch by 108 inch (3048 by 2743 mm) space requirement, below-grade mount.

Capacity:  7 bike, double side, 120 inch by 108 inch (3048 by 2743 mm) space requirement, free-standing/flange mount.

Capacity:  9 bike, double side 120 inch by 133 inch (3048 by 3378 mm) space requirement, below-grade mount.

Capacity:  9 bike, double side, 120 inch by 133 inch (3048 by 3378 mm) space requirement, free-standing/flange mount.

Capacity 11 bike, double side 120 inch by 158 inch (3048 by 4013 mm) space requirement, below-grade mount.

Capacity: 11 bike, double side 120 inch by 158 inch (3048 by 4013 mm) space requirement, free-standing/flange mount.

Finish: Polyester powder coat.

Color:  ________.

MATERIALS

** NOTE TO SPECIFIER **  Delete if not required.

Steel Tube: ASTM A 513, electric welded steel tubing.

** NOTE TO SPECIFIER **  Delete if not required.

Steel Pipe: ASTM A 500B steel pipe.

** NOTE TO SPECIFIER **  Delete paint finish if not required.

FINISH

Manufacturer's standard factory-applied polyester paint finishes using a powder coating heat-cured system.  Color as approved.

EXECUTION

EXAMINATION

Do not begin installation until substrates have been properly prepared.

If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

INSTALLATION

Install in accordance with manufacturer's instructions.

PROTECTION

Protect installed products until completion of project.

Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION