SECTION 02871

BICYCLE RACKS

Display hidden notes to specifier by using "Tools"/"Options"/"View"/"Hidden Text".

** NOTE TO SPECIFIER ** Saris Cycling Group; bicycle racks.
  .
  This section is based on the products of Saris Cycling Group, which is located at:
5253 Verona Rd.  
Madison, WI 53711
Toll Free Tel: 800-783-7257
Tel: 608-274-6550
Fax: 608-274-1702
Email: hfossen@saris.com
Web: www.sarisparking.com 
[ Click Here ] for additional information.
 Bicycle Racks:  SARIS metal racks for parking and storing bicycles: class II, and III. Formed tubing, welded and riveted grids.  Metal parking systems  
  .
  SECTION 02871 - BICYCLE RACKS, Copyright 2006, ARCAT, Inc.

- GENERAL

  - SECTION INCLUDES

** NOTE TO SPECIFIER **  Delete items below not required for project.

    - High capacity bicycle racks

Stretch Rack

Vertical Rack

  - RELATED SECTIONS

** NOTE TO SPECIFIER **  Delete any sections below not relevant to this project; add others as required.

    - Section 02871 – Bicycle Racks:  Installation location and coordination.

  - REFERENCES

** NOTE TO SPECIFIER **  Delete references from the list below that are not actually required by the text of the edited section.

    - American Society for Testing and Materials ASTM A513 - Standard Specification for Electric-Resistance-Welded Carbon and Alloy Steel Mechanical Tubing.

    - American Society for Testing and Materials ASTM A500B - Standard Specification for Cold-Formed Welded and Seamless Carbon Steel Structural Tubing in Rounds and Shapes.

  - SUBMITTALS

    - Submit under provisions of Section 01300.

    - [ [ Product Data ] ]:  Manufacturer's data sheets on each product to be used, including:

      - Preparation instructions and recommendations.

      - Storage and handling requirements and recommendations.

    - Shop Drawings:  Manufacturing details for each bicycle rack.

** NOTE TO SPECIFIER **  Delete selection samples if colors have already been selected.

    - Selection Samples:  For each finish product specified, two complete sets of color chips representing manufacturer's full range of available colors and patterns.

    - Verification Samples:  For each finish product specified, two samples, minimum size 6 inches (150 mm) square representing actual product, color, and patterns.

  - QUALITY ASSURANCE

    - Manufacturer Qualifications:

      - A firm experienced in manufacturing bicycle racks similar to those required for this project and with a record of successful in-service performance.

    - Installer Qualifications:

      - An experienced installer who has completed installation of bicycle racks similar in material, design, and extent to that indicated for this project and whose work has resulted in construction with a record of successful in-service performance.

    - Source Limitations: Obtain each color, finish, shape and type of bicycle rack from a single source with resources to provide components of consistent quality in appearance and physical properties.

** NOTE TO SPECIFIER **  Include a mock-up if the project size and/or quality warrant taking such a precaution.  The following is one example of how a mock-up on a large project might be specified.  When deciding on the extent of the mock-up, consider all the major different types of work on the project.

    - Mock-Up:  Provide a mock-up for evaluation of surface preparation techniques and application workmanship.

      - Install in areas designated by Architect.

      - Do not proceed with remaining work until workmanship and installation are approved by Architect.

      - Refinish mock-up area as required to produce acceptable work.

  - DELIVERY, STORAGE, AND HANDLING

    - Store products in manufacturer's unopened packaging until ready for installation.

    - Store and dispose of solvent-based materials, and materials used with solvent-based materials, in accordance with requirements of local authorities having jurisdiction.

  - PROJECT CONDITIONS

    - Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results.  Do not install products under environmental conditions outside manufacturer's absolute limits.

- PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer:  Saris Cycling Group; 5253 Verona Rd., Madison, WI 53711.  ASD. Toll Free TEL: (800) 783-7257. Te1: (608) 274-6550.  
Fax: (608) 274-1702.  Email:  info@sarisinfrastructure.com  
Web: http://www.sarisinfrastructure.com

** NOTE TO SPECIFIER **  Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

    - Substitutions:  Not permitted.

    - Requests for substitutions will be considered in accordance with provisions of Section 01600.

  - HIGH CAPACITY BICYCLE RACKS

** NOTE TO SPECIFIER **  Delete if not required.

    - Stretch Series: (items #8010; #8016; #8018; #8080; #8110; #8116; #8118; #8180)

      - Construction: 11 gauge (0.06 inch) (1.52 mm) steel for corner pieces and cross braces.

** NOTE TO SPECIFIER **  Delete capacities not required.

      - Capacity: 6 bike capacity, 18 inch (457 mm) spacing.

      - Capacity: 8 bike capacity, 13.5 inch (343 mm) spacing.

      - Capacity: 8 bike capacity, 18 inch (457 mm) spacing.

      - Capacity: 10 bike capacity 14.4 inch (366 mm) spacing.

** NOTE TO SPECIFIER **  Delete paragraph below if bike locking not required.

      - Locking Bar: 3/8 inch (9.5 mm) solid steel locking bar.

      - Finish: Polyester powder coat.

      - Color:  Black.

** NOTE TO SPECIFIER **  Delete if not required.

    - Vertical Series: (items #8023; #8024; #8043; #8044; #8033; #8034; #8063; #8064)

      - Construction: 11 gauge (0.06 inch) (1.52 mm) steel for corner pieces and cross braces.

** NOTE TO SPECIFIER **  Delete capacities not required.

      - Capacity:  3, 4, 5 bike capacity for single sided racks; 6, 8, 10 bike capacity for double sided racks

      - Standard bike spacing: 18” between bikes for 3, 4 bike single sided racks, and 6, 8 double sided racks; 15” between bikes for 5 bike single sided rack and 10 bike double sided rack

** NOTE TO SPECIFIER **  Delete paragraph below if bike locking not required.

      - Locking Bar: 3/8 inch (9.5 mm) solid steel locking loop.

      - Mount: Floor mount anchors recommended for single sided racks and REQUIRED for double sided racks.

      - Finish: Polyester powder coat.

      - Color:  Black.

  - MATERIALS

** NOTE TO SPECIFIER **  Delete if not required.

  - FINISH

    - Manufacturer's standard factory-applied polyester paint finishes using a powder coating heat-cured system.  Color as approved.

- EXECUTION

  - EXAMINATION

    - Do not begin installation until substrates have been properly prepared.

    - If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

  - INSTALLATION

    - Install in accordance with manufacturer's instructions.

  - PROTECTION

    - Protect installed products until completion of project.

    - Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION